## Slide 1: Kit Description and Chassis Attachments
IMPLEMENTATION SESSION

## Slide 2: Components of the Kit :
1 Chassis
2 Motors
1 Castor Wheel
2 Wheels
8 AA Batteries
2 AA Battery Holders
2 Battery Clips
ADXL335 accelerometer
1 U Clamp
1 Arduino Uno (Atmega 328)
USB to Serial Cable
2 Motor Driver Boards
1 Ultrasonic Sensor
20 M-M Jumper Wires
10 M-F Jumper Wires
Burg Strips
Screw Driver

## Slide 3
Components of the Kit :
1 Aqua Bot Chassis
Bluetooth Module
2 Propellers
2 micro DC motors
1 Dual Shaft Motor
2 Cycle Spokes

## Slide 4: Components of the Kit :

## Slide 5: Components of the Kit :

## Slide 6: Components of the Kit :
Chassis
USB to Arduino Cable

## Slide 7: Components of the Kit :

## Slide 8: Components of the Kit :

## Slide 9: Basic Chassis Attachments :
Attach the following to the chassis using screws and spacers and nuts:
  Castor wheel
  Motors to chassis
  Wheels to motor shaft
  Put the batteries in the battery holder
  Place the battery holder in the U-Clamp and then attach the U-Clamp to the lower part of the chassis.

## Slide 10: CASTOR WHEEL:
Attach the Castor wheel
to the chassis using screws and spacers

## Slide 15: Connections: Battery Series Connection
The two battery packs have to be connected in SERIES to collectively supply 12V.
The BLACK wire from one clip is connected to the RED wire of the other clip.
The other wires are connected to the power supply.

## Slide 16: Connections: Grounded Jumper Wire
A jumper wire is connected to the GROUND port in the power supply.
The other end is connected to the GROUND PIN on the Arduino.

## Slide 20: Attaching Boards :
Take the Arduino board and attach it using spacers on the upper side of the chassis .
Take the L293D motor driver board and attach it using spacers on the upper back side of the chassis.

## Slide 29: Motor Assembly:
Attach the motors to the L- clamp.
Fix the wheels with the motors using screws.

## Slide 40: Connections: L293D J3 Pin
The Arduino board uses a 5V supply to function.
The J3 pin on the L293D board supplies 12V voltage to Arduino board, hence strictly should NOT be used.
The pin C1 (beside J3 pin) should be USED at all times.

## Slide 41: Connections: Arduino Power Supply
The Arduino board can be powered using two sources – A USB cable or the L293D board.
The power supply mode can be switched using the PWR-SEL pins.
The jumper pin should be on the SEL side at all times.

## Slide 42: Connections: Motors -> L293D
The Motors have a RED wire and a BLACK wire.
Each of these wires is to be connected to MOT-A and MOT-B ports on the L293D.
The BLACK wire is to be connected to the side the port labels are printed on as illustrated below.

## Slide 44: Connections: Arduino -> L293D
The following connections have to be made between the two boards :
A -> PIN 5
A’ -> PIN 4
B -> PIN 3
B’ -> PIN 2
Note : The pins mentioned are the Digital Pins and not the Analog ones.

## Slide 47: IDE Installation
IMPLEMENTATION SESSION

## Slide 48: Installing Arduino IDE :
Open “Robotix” Folder.
Open “softwares” Folder.
Run arduino-1.0.5-windows.exe if using a PC
Or copy arduino.app to your desktop for MAC
Install the software by following the on-screen instructions.

## Slide 49: Installing Drivers:
Open folder Robotix
Choose your version of driver depending on your OS
Extract the files
Run CDM v2.08.30 WHQL Certified.exe or mac os x 32 bit----FTDIUSBSerialDriver_v2_2_18.dmg (depending on your version of mac OS)
Install the driver by following the on-screen instructions.

## Slide 50: Settings in IDE:
Open Arduino IDE .
Go to : Tools -> board
  Select Arduino Duemilanove w/ ATmega328
Connect your Arduino using USB
Go to Control Panel ->Device Manager ->Ports
  See the port in which USB COM is connected.
Go to : Tools -> Port
  Select same COM Port as shown in device manager.
You are now ready to upload programs.

## Slide 51: Uploading Program:
Your connections are now ready.
Make sure to remove the jumper wire to the GND pin on the Arduino board coming from L293D board before uploading.
Connect the USB to the USB port.
Switch on the USB communication.
Open Arduino IDE.
Compile and upload the program.